## Slide 1: Frogger (for the Spartan 3E-500 development board)
ECE 525.442 FPGA Microprocessor Design
Erik Lee, Edward Jones, Emily Kan

## Slide 2: Outline
Introduction
Background
Design
Implementation & Verification
Results & Analysis
Conclusion
References

## Slide 3: Introduction

## Slide 4: Background VGA controller
Display 640 x 480
50MHz board clock  25MHz pixel clock
  Horizontal sync and Vertical sync pulses driven by 25MHz clock
  8-bit color vector
    2-bit blue
    3-bit green
    3-bit red
VGA Port
Hsync
Vsync
Red
Green
Blue
Game Module
Horizontal sync
Vertical sync
Red
Green
Blue
640
480

## Slide 5: Background PS/2 Keyboard
  Component Instantiation of
    PS/2 driver core given
    Basic connection and logic
      Output clock to keyboard
      Input keypress data from keyboard (11-bits)
      Map data to frog direction
Up | Down | Left | Right
Game Module |  |  | 
Keyboard
Data
Clock
PS/2 Module
Data
Clock

## Slide 6: Design Overview
Block Diagram
    Object generator
    Frog generator
    Background generator
    Frog Location
    Collision Detection – Implements Rules and Interactions

## Slide 7: Design
Structure of Frogger
  Background
    Road
    Grass
    River
  Objects
    Cars
    Logs
    Frog

## Slide 8: Game Layout
Erik
Structure of the game
Background
Objects
Images of early stages of the game
Images of final product of the game

## Slide 9: Design Rules Implementation
Finite State Machine - Mealy
Define outputs
  Dead
  Reset
  On a log
Define inputs
  Object colors
  Background colors
  Frog position
Define states
Define transitions (interactions with objects and background)
Notes: Finite State Machine – 5 states
Define Outputs:
Flag when frog is hit by a car
Flag when frog is on a log
Flag for resetting frog back to homebase
Define Inputs:
4 corners of frog (xy-pixel)
Object color
Background color
Frog Position
Define states:
5 states – onGrass, onRoad, onRiver, Dead, Win
Transitions

## Slide 10: Design Finite State Machine Diagram
onGrass_state
onRoad_state
dead_state
win_state
All Bgcolor=black /
Dead=‘0’
All Bgcolor=green/
Dead=‘0’
Any Objcolor/=black /
Dead=‘0’
Counter< 3secs /
Dead=‘1’
Counter>=3secs/
Dead=‘0’ Reset=‘1’
All objcolor=black/
Dead=‘0’
All Bgcolor=blue /
Dead=‘0’
Any objcolor=green and Row=0 /
Dead=‘0’
Counter< 3secs /
win=‘1’
onRiver_state
Any objcolor=brown/
OnLog=‘1’
Any Bgcolor=black /
Dead=‘0’
All
Bgcolor=green/
Dead=‘0’
Counter>=3secs/
Reset=‘1’

## Slide 11: Implementation & Verification
VGA drivers
  2 Counters ( pixel count)
  35 DFFs
  2 Adders/Subtractors
  8 Comparators
PS/2 Keyboard driver
  1 Counter
  20 DFFs
  1 Xor
Background Generator
  8 DFFs
Object Generator
  2 Accumulators
  8 DFFs
  1 Adder/Subtractor
  5 Comparators
Frog Generator
  1 Counter
  8 DFFs
  5 Comparators
Frog Location
  1 ROM (frog Row location)
  42 DFFs
  3 Adders/Subtractors
  5 Comparators
1 Finite State Machine
  5 states, 61 transitions, 22 inputs, 3 outputs
  1 Counter
  64 DFFs
  8 Comparators

## Slide 12: Results and Analysis
Resource | Quantity
ROM | 1
Adders/ Subtractors | 29
Counters | 13
Accumulators | 48
Registers | 96
Comparators | 156
Xors | 8
Flip-Flops | 964
Inputs | 15
Outputs | 10
Device Utilization | 
Number of Slices | 1345/4656 =(28%)
Number of Slice Flip-Flops | 964/9312 = (10%)
Number of 4 input LUTs | 2572/9312 = (27%)

## Slide 13: Demonstration

## Slide 14: Conclusion

## Slide 15: References
NEXYS2 Reference Manual
http://www.digilentinc.com/showcase/contests/designcontest.cfm?contestid=8
Need references for keyboard vhdl code
http://www.pyroelectro.com/tutorials/ps2_keyboard_interface/theory_ps2.html